## Slide 1: Lunch and Learn: Environmental Review of Commercial Real Estate Community Capital Development Corporation 5475 Rings Road Dublin, OH
R. Curtis Spence, PE
Spence Environmental Consulting, Inc.
January 20, 2026

## Slide 2: What is Environmental Risk?
Carcinogenic (cancer causing) and non-carcinogenic (damage to the liver, kidneys, nervous system, and respiratory tract, and developmental issues) risk from exposures to chemical contaminants in the air, water, and soil.
Exposure pathways include inhalation, ingestion and dermal contact.
  Inhalation of contaminated air (vapor intrusion into structures).
  Ingestion of contaminated groundwater.
  Dermal contact with contaminated soil.
Carcinogenic and non-carcinogenic risk may be isolated to the immediate location of the chemical contaminants (i.e., spill location) or may extend miles from the source area (groundwater contaminant plume).

## Slide 3: What is Excessive Environmental Risk?
Concentrations of chemical contaminants in soil, groundwater and indoor air exceed standards published by the U.S. EPA, Ohio EPA Voluntary Action Program (VAP), and Ohio Bureau of Underground Storage Tank Regulations (BUSTR). Standards are typically based on 1 in 100,000 excessive cancer risk and a cumulative hazard quotient of 1 for non-carcinogenic risk.
Standards are published for both residential and commercial exposure scenarios and are typically based on 30 years of exposure.
Site specific standards or target levels can also be developed following procedures published by the U.S. EPA, Ohio EPA and BUSTR.

## Slide 4: Mitigation of Excessive Environmental Risk
Source removal (soil excavation and groundwater extraction).
Contaminant reduction to acceptable concentrations through treatment including: chemical oxidation, biological treatment; activated carbon adsorption; and thermal processes. Includes in situ and ex situ treatment.
Engineering controls to prevent exposures including: vapor intrusion barriers; sub-slab depressurization; clean soil cover; and paved surfaces.
Environmental covenants (deed restrictions) prohibiting residential use, potable use of groundwater, etc.

## Slide 5: Evaluating Environmental Risk
Step 1: Perform an assessment to determine if the subject property has the potential for excessive environmental risk. This includes the presence, likely presence or material threat of a release of hazardous substances and petroleum products.
SBA Records Search with Risk Assessment (SBA SOP 50 10 8) (Apparent Low Risk Sites – not Environmentally Sensitive per Appendix 6 in SBA SOP 50 10 8)
Environmental Transaction Screen (ASTM E1528-22) (Sites where CERCLA liability protection is not desired)
Phase I Environmental Site Assessment (ASTM E1527-23) (Industry standard for “All Appropriate Inquiry under U.S. EPA Brownfield Program” including CERCLA liability protection)

## Slide 9: Evaluating Environmental Risk
State and Federal Environmental Databases (1980’s to Present)
  Superfund Sites (National Priorities List) and other CERCLA (Comprehensive Environmental Response, Compensation, and Liability Act) Sites (1.0 and 0.5 Miles)
  Hazardous Waste (RCRA) Corrective Action, TSD, and Generator Sites (1.0 and 0.5 Miles and Subject and Adjoining Properties)
  Emergency Response Notification System (Subject Property)
  Landfills and Solid Waste Facilities (0.5 Miles)
  Leaking Underground Storage Tank Sites (0.5 Miles)
  Registered Underground Storage Tank Sites (Subject and Adjoining Properties)
  Voluntary Action Program Sites (0.5 Miles)
  Federal and State Institutional and Engineering Control Registries (Subject Property)
Historical Records (First Developed Use to Present)
  Historical Aerial Photography
  City Directory Records
  Fire Insurance Maps
  Historical Topographic Maps

## Slide 10: Evaluating Environmental Risk
Interviews:
  Site Owner
  Site Occupants or Managers
  Local Government Officials
    Fire Department
    Health Department
    Building Department
    Local Trustees or Zoning Officers
Site Features:
  Topography
  Geology and Hydrogeology
Site Inspection:
  Current Site Usage and Development
  Use of Hazardous Substances and Petroleum Products
  Visible Evidence of Historical Usage
  Housekeeping and Engineering Controls
  Adjacent/Nearby Site Usage

## Slide 11: Phase I Environmental Site Assessment (ASTM E1527-23)
Environmental Database
Historical Records
Interviews of Past and Present Owners and Occupants via Questionnaires
Interview/Questionnaire of Report User for Prior Site Knowledge, Environmental Liens, Use Limitations, Environmental Impact on Sale Price
Interviews of Local Public Officials
Visual Inspection of Subject Site and Adjoining Properties (Photo Documentation)
Detailed Report of Collected Data and Identification of RECs, CRECs, HRECs, and BERs.
Non-Scope Considerations including Asbestos, Wetlands, Mold, Lead-Based Paint, and Lead in Drinking Water may be added to the Scope of Work.

## Slide 12: SBA Gasoline Station Loans
Per SBA SOP 50 10 8, Appendix 7, the following work must be completed.
  Phase I Environmental Site Assessment
  UST Records including BUSTR Registration, PUSTRCB Insurance Certificate, Compliance Inspections and Testing Records
  Repair or Replacement of any Failed, Leaking or otherwise Defective Equipment
  Phase II Environmental Site Assessment (if required)

## Slide 13: What are the Findings of an Environmental Assessment?
SBA RS/RA: Low, Elevated or High Risk
Transaction Screen: Potential Environmental Concerns
Phase I ESA: REC, CREC, HREC, BER

## Slide 14: Recognized Environmental Condition (REC)
A Recognized Environmental Condition (REC) is:
  The presence of hazardous substances or petroleum products in, on, or at the subject property due to a release to the environment;
  The likely presence of hazardous substances or petroleum products in, on, or at the subject property due to a release or likely release to the environment; or
  The presence of hazardous substances or petroleum products in, on, or at the subject property under conditions that pose a material threat of a future release to the environment.
.

## Slide 15: Recognized Environmental Condition (REC)
Potential RECs:
  Use or Storage of Hazardous Materials or Petroleum Products
  Underground and Aboveground Storage Tanks
  Dry Cleaning
  Underground Hydraulic Lifts
  Manufacturing Facilities
  Wood Finishing
  Metal Plating
  Chemical Manufacturing and Distribution
  Known Spills
  Hazardous Waste Generators
  Solid Waste Disposal

## Slide 16: Controlled Recognized Environmental Condition (CREC)
A Controlled Recognized Environmental Condition (CREC) is a REC at the subject property that has been addressed to the satisfaction of the applicable regulatory authority or authorities with hazardous substances or petroleum products allowed to remain in place subject to implementation of required controls. In the case of self-directed actions, documentation that the REC satisfies risk-based criteria established by the applicable regulatory authority or authorities.
A past release that previously qualified as a CREC may no longer constitute a CREC if new conditions or information have been identified such as a change in regulatory criteria, a change of use at the subject property, or a subsequently identified migration pathway that was not previously known or evaluated.

## Slide 17: Historical Recognized Environmental Condition (HREC)
A Historical Recognized Environmental Condition (HREC) is a previous release of hazardous substances or petroleum products affecting the subject property that has been addressed to the satisfaction of the applicable regulatory authority or authorities and meeting unrestricted use criteria established by the applicable regulatory authority or authorities without subjecting the subject property to any controls (for example, activity and use limitations or other property use limitations). A HREC is not a REC.
A past release that qualified as a HREC may no longer qualify as a HREC if new conditions or information have been identified such as a change in regulatory criteria or a subsequently identified migration pathway that was not previously known or evaluated.

## Slide 18: Business Environmental Risk (BER)
A Business Environmental Risk (BER) is a risk which can have a material environmental or environmentally-driven impact on the business associated with the current or planned use of commercial real estate, not necessarily related to those environmental issues required to be investigated in this practice.
A BER may include hazardous substances and petroleum products storage and use, asbestos, wetlands, lead-based paint, and environmental compliance concerns.

## Slide 19: Recognized Environmental Condition (REC) Environmental Databases

## Slide 20: Recognized Environmental Condition (REC) Environmental Databases

## Slide 21: Recognized Environmental Condition (REC) City Directories
1959 1999

## Slide 22: Recognized Environmental Condition (REC) Aerial Photographs
1971 1980

## Slide 23: Recognized Environmental Condition (REC) Sanborn™ Fire Insurance Maps

## Slide 24: Recognized Environmental Condition (REC)
Sanborn™ Fire Insurance Maps
(1896 to 1914)

## Slide 25: Phase II Environmental Site Assessments
Step 2: Determine if a Recognized Environmental Condition (REC) has resulted in excessive environmental risk.
Collect soil vapor, indoor air, soil, and groundwater samples and analyze collected samples for the chemicals of concern associated with the identified hazardous substances and/or petroleum products.
Common equipment used during a Phase II ESA include sub-slab and indoor air sampling equipment (vapor pins and summa canisters), soil sampling equipment (hydraulic sampling probe), groundwater monitoring wells, ground-penetrating radar, electromagnetic instruments, and hand sampling equipment.

## Slide 26: Indoor Air Sampling

## Slide 27: Sub-Slab Soil Vapor Sampling

## Slide 28: Sub-Slab Soil Vapor Sampling

## Slide 29: Hydraulic Sampling Probe

## Slide 30: Hydraulic Sampling Probe

## Slide 31: Rotary Drill Rig

## Slide 32: Groundwater Monitoring Wells

## Slide 33: Ground Penetrating Radar

## Slide 34: Ground Penetrating Radar

## Slide 35: How are Leaking Underground Storage Tank Sites in Ohio Evaluated? (BUSTR Corrective Action)
Required if a release is suspected or confirmed at a BUSTR regulated underground storage tank site.
Tier 1 Evaluation: Site assessment to define the extent of soil and groundwater impacts similar to a Phase II ESA except permanent groundwater monitoring wells are required.
Tier 2 Evaluation: Environmental risk assessment including evaluation of: groundwater fate and transport; soil to groundwater leaching; and soil and groundwater to indoor air exposure pathways.
A Remedial Action Plan is prepared after the Tier 2 Evaluation and may include soil and/or groundwater remediation.

## Slide 36: Site Remediation
Goal: Lower environmental risk to acceptable levels (below generic published standards or site specific target levels)
Soil: Landfilling, Bioremediation, Vapor Extraction, Chemical Oxidation, Thermal Oxidation, Stabilization
Groundwater: Extraction and Off-Site Treatment, Carbon Adsorption, Air Stripping, Bioremediation, Chemical Oxidation, Natural Attenuation, Reactive Barriers
Soil Vapors: Vapor Extraction
Land Use Restrictions: No Groundwater Use, No Residential Use, No Basements, No Excavations
Engineering Controls: Vapor Intrusion Barrier, Sub-Slab Depressurization, Pavement, Clean Soil Cover

## Slide 37: Soil Excavation and Disposal

## Slide 38: Soil Excavation and Disposal

## Slide 39: Chemical Oxidation and Bioremediation

## Slide 40: Enhanced Fluid Recovery (EFR)

## Slide 41: Sub-Slab Vapor Intrusion Mitigation System

## Slide 42: Vapor Intrusion Barrier

## Slide 43: Questions ?